## Slide 1
Chapter 3:
Sequential Logic Design
Digital Design &
Computer Architecture
Sarah Harris & David Harris

## Slide 2
Chapter 3 :: Topics
State Elements
  Bistable Circuit
  SR Latch
  D Latch
  D Flip-Flop
  Variations
Synchronous Sequential Logic
Finite State Machines
  Moore
  Mealy
  Factored
Timing of Sequential Logic
  Clock Skew
  Synchronization
Parallelism

## Slide 3
Chapter 3: Sequential Logic
State Elements

## Slide 4
Outputs of sequential logic depend on current and prior input values – it has memory.
Some definitions:
  State: all the information about a circuit necessary to explain its future behavior
  Latches and flip-flops: state elements that store one bit of state
  Synchronous sequential circuits: Sequential circuits using flip-flops sharing a common clock
Introduction

## Slide 5
Give sequence to events
Have memory (short-term)
Use feedback from output to input to store information
Sequential Circuits

## Slide 6
State: everything about the prior inputs to the circuit necessary to predict its future behavior
  Usually just 1 bit, the last value captured
State elements store state
  Bistable circuit
  SR Latch
  D Latch
  D Flip-flop
State Elements

## Slide 7
Chapter 3: Sequential Logic
Bistable Circuit

## Slide 8
Fundamental building block of other state elements
Two outputs: Q, Q
No inputs
Bistable Circuit
Back-to-back inverters
Cross-coupled inverters
Same circuit!

## Slide 9
Consider the two possible cases:
  Q = 0:
  then Q = 1, Q = 0 (consistent)
  Q = 1:
  then Q = 0, Q = 1 (consistent)
Stores 1 bit of state in the state variable, Q (or Q)
But there are no inputs to control the state
Bistable Circuit Analysis

## Slide 10
Chapter 3: Sequential Logic
SR Latch

## Slide 11
SR Latch
Consider the four possible cases:
  S = 1, R = 0
  S = 0, R = 1
  S = 0, R = 0
  S = 1, R = 1
SR (Set/Reset) Latch

## Slide 12
  S = 1, R = 0:
  then Q = 1 and Q = 0
  Set the output
  S = 0, R = 1:
  then Q = 0 and Q = 1
  Reset the output
SR Latch Analysis

## Slide 13
  S = 0, R = 0:
  then Q = Qprev
  Memory!
  S = 1, R = 1:
  then Q = 0, Q = 0
  Invalid State
  Q ≠ NOT Q
SR Latch Analysis

## Slide 14
SR stands for Set/Reset Latch
  Stores one bit of state (Q)
Control what value is being stored with S, R inputs
  Set: Make the output 1
  S = 1, R = 0, Q = 1
  Reset: Make the output 0
  S = 0, R = 1, Q = 0
  Memory: Retain value
  S = 0, R = 0, Q = Qprev
Must do something to avoid invalid state (when S = R = 1)
SR Latch

## Slide 15
Chapter 3: Sequential Logic
D Latch

## Slide 16
Two inputs: CLK, D
  CLK: controls when the output changes
  D (the data input): controls what the output changes to
Function
  When CLK = 1,
  D passes through to Q (transparent)
  When CLK = 0,
  Q holds its previous value (opaque)
Avoids invalid case when
Q ≠ NOT Q
D Latch

## Slide 17
D Latch Internal Circuit

## Slide 18
Chapter 3: Sequential Logic
D Flip-Flop

## Slide 19
Inputs: CLK, D
Function:
  Samples D on rising edge of CLK
    When CLK rises from 0 to 1, D passes through to Q
    Otherwise, Q holds its previous value
  Q changes only on rising edge of CLK
Called edge-triggered
  Activated on the clock edge
D Flip-Flop

## Slide 20
Two back-to-back D latches (L1 and L2) controlled by complementary clocks
When CLK = 0
  L1 is transparent
  L2 is opaque
  D passes through to N1
When CLK = 1
  L2 is transparent
  L1 is opaque
  N1 passes through to Q
Thus, on the edge of the clock (when CLK rises from 0 1)
  D passes through to Q
D Flip-Flop Internal Circuit

## Slide 21
D Latch vs. D Flip-Flop
D Latch
D Flip-flop

## Slide 22
Chapter 3: Sequential Logic
Variations on a Flop

## Slide 23
Registers: One or More Flip-flops
4-bit Register
4-bit Register
Easier to draw!
Two ways to draw a register

## Slide 24
Inputs: CLK, D, EN
  The enable input (EN) controls when new data (D) is stored
Function
  EN = 1: D passes through to Q on the clock edge
  EN = 0: the flip-flop retains its previous state
Enabled Flip-Flops

## Slide 25
Inputs: CLK, D, Reset
Function:
  Reset = 1: Q is forced to 0
  Reset = 0: flip-flop behaves as ordinary D flip-flop
Resettable Flip-Flops

## Slide 26
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop
Synchronously resettable flip-flop?
Resettable Flip-Flops

## Slide 27
Inputs: CLK, D, Set
Function:
  Set = 1: Q is set to 1
  Set = 0: the flip-flop behaves as ordinary D flip-flop
Settable Flip-Flops

## Slide 28
Chapter 3: Sequential Logic
Synchronous Sequential Logic

## Slide 29
Sequential circuits: all circuits that aren’t combinational
A problematic circuit:
    No inputs and 1-3 outputs
    Astable circuit, oscillates
    Period depends on inverter delay
    It has a cyclic path: output fed back to input
Sequential Logic

## Slide 30
Breaks cyclic paths by inserting registers
Registers contain state of the system
State changes at clock edge: system synchronized to the clock
Rules of synchronous sequential circuit composition:
  Every circuit element is either a register or a combinational circuit
  At least one circuit element is a register
  All registers receive the same clock
  Every cyclic path contains at least one register
Two common synchronous sequential circuits
  Finite State Machines (FSMs)
  Pipelines
Synchronous Sequential Logic Design

## Slide 31
Breaks cyclic paths by inserting registers
Registers contain state of the system
State changes at clock edge: system synchronized to the clock
Rules of synchronous sequential circuit composition:
  Every circuit element is either a register or a combinational circuit
  At least one circuit element is a register
  All registers receive the same clock
  Every cyclic path contains at least one register
Two common synchronous sequential circuits
  Finite State Machines (FSMs)
  Pipelines
Synchronous Sequential Logic Design

## Slide 32
Chapter 3: Sequential Logic
FSMs:
Finite State Machines

## Slide 33
Consists of:
  State register
    Stores current state
    Loads next state at clock edge
  Combinational logic
    Computes the next state
    Computes the outputs
Finite State Machine (FSM)

## Slide 34
Next state determined by current state and inputs
Two types of finite state machines differ in output logic:
  Moore FSM: outputs depend only on current state
  Mealy FSM: outputs depend on current state and inputs
Finite State Machines (FSMs)

## Slide 35
Next state determined by current state and inputs
Two types of finite state machines differ in output logic:
  Moore FSM: outputs depend only on current state
  Mealy FSM: outputs depend on current state and inputs
Finite State Machines (FSMs)

## Slide 36
FSM Design Procedure
Identify inputs and outputs
Sketch state transition diagram
Write state transition table and output table
  Moore FSM: write separate tables
  Mealy FSM: write combined state transition and output table
Select state encodings
Rewrite state transition table and output table with state encodings
Write Boolean equations for next state and output logic
Sketch the circuit schematic

## Slide 37
FSM Design Procedure
Identify inputs and outputs
Sketch state transition diagram
Write state transition table and output table
  Moore FSM: write separate tables
  Mealy FSM: write combined state transition and output table
Select state encodings
Rewrite state transition table and output table with state encodings
Write Boolean equations for next state and output logic
Sketch the circuit schematic

## Slide 38
Chapter 3: Sequential Logic
Moore FSM Example

## Slide 39
Traffic light controller
  Traffic sensors: TA, TB (TRUE when there’s traffic)
  Lights: LA, LB
FSM Example

## Slide 40
Inputs: CLK, Reset, TA, TB
Outputs: LA, LB
FSM Black Box

## Slide 41
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs
FSM State Transition Diagram

## Slide 42
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0
FSM State Transition Table
S : Current State
S’: Next State

## Slide 43
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
FSM Encoded State Transition Table
S0
S1
S2
S2
S3
S0
S'1 = S1S0 + S1S0TB + S1S0TB = S1S0 + S1S0 = S1 Å S0
S'0 = S1S0TA + S1S0TB
S1
S2
S3
S2
S0
S0

## Slide 44
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
FSM Output Table
LA1 = S1S0 + S1S0 = S1
LA0 = S1S0
LB1 = S1S0 + S1S0 = S1
LB0 = S1S0
S0
S1
S2
S3
green
yellow
red
red
red
red
green
yellow

## Slide 45
FSM Schematic
State Register
Next State
Current State
Next State Logic
Output Logic
LA1 = S1
LA0 = S1S0
LB1 = S1
LB0 = S1S0
S'1 = S1 Å S0
S'0 = S1S0TA + S1S0TB

## Slide 46
FSM Timing Diagram

## Slide 47
FSM Timing Diagram

## Slide 48
State Encodings
Binary encoding:
  i.e., for four states, 00, 01, 10, 11
One-hot encoding
  One state bit per state
  Only one state bit HIGH at once
  i.e., for 4 states, 0001, 0010, 0100, 1000
  Requires more flip-flops
  Often next state and output logic is simpler

## Slide 49
S’3 = S3S2S1S0TB
NO!
Current State |  |  |  | Inputs |  | Next State |  |  | 
S3 | S2 | S1 | S0 | TA | TB | S’3 | S’2 | S’1 | S’0
0 | 0 | 0 | 1 | 0 | X | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | X | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | X | X | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | X | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | X | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | X | X | 0 | 0 | 0 | 1
State | 1-Hot Encoding
S0 | 0001
S1 | 0010
S2 | 0100
S3 | 1000
1-Hot State Encoding Example
S’3 = S2TB
S’2 = S1 + S2TB
S’1 = S0TA
S’0 = S0TA + S3
S0
S1
S2
S2
S3
S0
S1
S2
S3
S2
S0
S0

## Slide 50
Chapter 3: Sequential Logic
Mealy FSM Example

## Slide 51
Moore vs. Mealy FSMs
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it. The snail smiles whenever the last two digits it has crawled over are 01. Design Moore and Mealy FSMs of the snail’s brain.

## Slide 52
State Transition Diagrams

## Slide 53
S1’ = S0A
S0’ = A
Moore FSM State Transition Table
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S1’ = S1S0A
S0’ = A
Current State |  | Inputs | Next State | 
S1 | S0 | A | S'1 | S'0
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0

## Slide 54
Moore FSM Output Table
State | Encoding
S0 | 00
S1 | 01
S2 | 10
Y = S1 S0
Current State |  | Output
S1 | S0 | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
Y = S1

## Slide 55
Mealy State Transition & Output Table
State | Encoding
S0 | 0
S1 | 1
S0’ = A
Y = S0 A
Current State | Input | Next State | Output
S0 | A | S'0 | Y
0 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 56
Moore FSM Schematic
Next State Equations
S1’ = S0A
S0’ = A
Output Equation
Y = S1

## Slide 57
Mealy FSM Schematic
Next State Equation
S0’ = A
Output Equation
Y = S0A

## Slide 58
Mealy FSM: asserts Y immediately when input pattern 01 is detected
Moore FSM: asserts Y one cycle after input pattern 01 is detected
Moore and Mealy Timing Diagram

## Slide 59
Chapter 3: Sequential Logic
Factored FSMs

## Slide 60
Factoring FSMs
Break complex FSMs into smaller interacting FSMs
Example: Modify traffic light controller to have Parade Mode.
  Two more inputs: P, R
  When P = 1, enter Parade Mode & Bravado Blvd light stays green
  When R = 1, leave Parade Mode

## Slide 61
Unfactored FSM
Factored FSM
Parade FSMs

## Slide 62
Unfactored FSM

## Slide 63
Factored FSM

## Slide 64
Chapter 3: Sequential Logic
Timing

## Slide 65
Flip-flop samples D at clock edge
D must be stable when sampled
Similar to a photograph, D must be stable around clock edge
Timing

## Slide 66
Setup time: tsetup = time before clock edge data must be stable (i.e. not changing)
Hold time: thold = time after clock edge data must be stable
Aperture time: ta = time around clock edge data must be stable (ta = tsetup + thold)
Input Timing Constraints

## Slide 67
Propagation delay: tpcq = time after clock edge that Q is guaranteed to be stable (i.e., to stop changing): maximum delay
Contamination delay: tccq = time after clock edge that Q might be unstable (i.e., start changing): minimum delay
Output Timing Constraints

## Slide 68
Synchronous sequential circuit inputs must be stable during aperture (setup and hold) time around clock edge
Specifically, inputs must be stable
  at least tsetup before the clock edge
  at least until thold after the clock edge
Dynamic Discipline

## Slide 69
The delay between registers has a minimum and maximum delay, dependent on the delays of the circuit elements
Dynamic Discipline

## Slide 70
Depends on the maximum delay from register R1 through combinational logic to R2
The input to register R2 must be stable at least tsetup before clock edge
Setup Time Constraint
Tc ≥ tpcq + tpd + tsetup
tpd ≤ Tc – (tpcq + tsetup)
(tpcq + tsetup):
sequencing overhead
Also called:
Cycle Time Constraint

## Slide 71
Depends on the minimum delay from register R1 through the combinational logic to R2
The input to register R2 must be stable for at least thold after the clock edge
Hold Time Constraint
thold < tccq + tcd
tcd > thold - tccq

## Slide 72
Timing Analysis
Calculate both constraints:
  Setup time constraint (aka cycle time constraint)
  Hold time constraint
If the hold time constraint isn’t met, the circuit won’t work reliably at any frequency

## Slide 73
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 25) ps > 70 ps ? No!
Timing Analysis Example
Flip-Flops
Logic delays:
per gate
Tc ≥ tpcq + tpd + tsetup
Won’t run reliably at any frequency

## Slide 74
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 50) ps > 70 ps ? Yes!
Timing Analysis Example
Flip-Flops
Logic delays:
per gate
Add buffers on short paths
How to fix?

## Slide 75
Chapter 3: Sequential Logic
Clock Skew

## Slide 76
The clock doesn’t arrive at all registers at same time
Skew: difference between two clock edges
Perform worst case analysis to guarantee dynamic discipline is not violated for any register – many registers in a system!
Clock Skew

## Slide 77
In the worst case, CLK2 is earlier than CLK1
Setup Time Constraint with Skew
Tc ≥ tpcq + tpd + tsetup + tskew
tpd ≤ Tc – (tpcq + tsetup + tskew)
Tc - tskew ≥ tpcq + tpd + tsetup

## Slide 78
In the worst case, CLK2 is later than CLK1
Hold Time Constraint with Skew
tccq + tcd > thold + tskew
tcd > thold + tskew – tccq

## Slide 79
Chapter 3: Sequential Logic
Synchronization

## Slide 80
Violating the Dynamic Discipline
Asynchronous (for example, user) inputs might violate the dynamic discipline

## Slide 81
Metastability
Bistable devices: two stable states, and a metastable state between them
Flip-flop: two stable states (1 and 0) and one metastable state
If flip-flop lands in metastable state, could stay there for an undetermined amount of time

## Slide 82
Flip-Flop Internals
Flip-flop has feedback: if Q is somewhere between 1 and 0, cross-coupled gates drive output to either rail (1 or 0)
Metastable signal: if it hasn’t resolved to 1 or 0
If flip-flop input changes at random time, probability that output Q is metastable after waiting some time, t:
P(tres > t) = (T0/Tc ) e-t/τ
tres : time to resolve to 1 or 0
T0, τ : properties of the circuit

## Slide 83
Metastability
Intuitively:
  T0/Tc: probability input changes at a bad time (during aperture time)
P(tres > t) = (T0/Tc ) e-t/τ
  τ: time constant for how fast flip-flop moves away from metastability
P(tres > t) = (T0/Tc ) e-t/τ
If flip-flop samples metastable input, if you wait long enough (t), the output will have resolved to 1 or 0 with high probability.

## Slide 84
Synchronizers
Asynchronous inputs are inevitable (user interfaces, systems with different clocks interacting, etc.)
Synchronizer goal: make the probability of failure (the output Q still being metastable) low
Synchronizer cannot make the probability of failure 0

## Slide 85
Synchronizer Internals
Synchronizer: built with two back-to-back flip-flops
Suppose D is transitioning when sampled by F1
Internal signal D2 has (Tc - tsetup) time to resolve to 1 or 0

## Slide 86
Synchronizer Internals
Synchronizer: built with two back-to-back flip-flops
Suppose D is transitioning when sampled by F1
Internal signal D2 has (Tc - tsetup) time to resolve to 1 or 0

## Slide 87
Synchronizer Probability of Failure
For each sample, probability of failure is:
P(failure) = (T0/Tc ) e-(Tc - tsetup)/τ

## Slide 88
Synchronizer Mean Time Between Failure
If asynchronous input changes once per second, probability of failure per second is P(failure).
If input changes N times per second, probability of failure per second is:
P(failure)/second = (NT0/Tc) e-(Tc - tsetup)/τ
Synchronizer fails, on average, 1/[P(failure)/second]
Called mean time between failures, MTBF:
MTBF = 1/[P(failure)/second] = (Tc/NT0) e(Tc - tsetup)/τ

## Slide 89
Example Synchronizer
Suppose: Tc = 1/500 MHz = 2 ns τ = 200 ps
T0 = 150 ps tsetup = 100 ps
N = 10 events per second
What is the probability of failure? MTBF?
P(failure) = (150 ps/2 ns) e-(1.9 ns)/200 ps
= 5.6 × 10-6
P(failure)/second = 10 × (5.6 × 10-6 )
= 5.6 × 10-5 / second
MTBF = 1/[P(failure)/second] ≈ 5 hours
P(failure)/second = (NT0/Tc) e-(Tc - tsetup)/τ
MTBF = 1/[P(failure)/second]

## Slide 90
Chapter 3: Sequential Logic
Parallelism

## Slide 91
Parallelism
Two types of parallelism:
  Spatial parallelism
    duplicate hardware performs multiple tasks at once
  Temporal parallelism
    task is broken into multiple stages
    also called pipelining
    for example, an assembly line

## Slide 92
Parallelism
Token: Group of inputs processed to produce group of outputs
Latency: Time for one token to pass from start to end
Throughput: Number of tokens produced per unit time
Parallelism increases throughput

## Slide 93
Parallelism Example
Ben Bitdiddle bakes cookies to celebrate traffic light controller installation
  5 minutes to roll cookies
  15 minutes to bake
What is the latency and throughput without parallelism?
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 tray/ 1/3 hour = 3 trays/hour

## Slide 94
Parallelism Example
What is the latency and throughput if Ben uses parallelism?
  Spatial parallelism: Ben asks Allysa P. Hacker to help, using her own oven
  Temporal parallelism:
    two stages: rolling and baking
    He uses two trays
    While first batch is baking, he rolls the second batch, etc.

## Slide 95
Spatial Parallelism
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 2 trays/ 1/3 hour = 6 trays/hour

## Slide 96
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 trays/ 1/4 hour = 4 trays/hour
Using both techniques, the throughput would be 8 trays/hour
Temporal Parallelism

## Slide 97
Digital Design and Computer Architecture Lecture Notes
© 2021 Sarah Harris and David Harris
These notes may be used and modified for educational and/or non-commercial purposes so long as the source is attributed.
About these Notes
97